## Slide 1: PHC 6194-spatial epidemiology Coordinate systems and Map Project Xiaohui Xu, Ph.D Department of Epidemiology

## Slide 2: Acknowledgement
This lecture is modified based on Dr. YouLiang Qiu’ lecture slides from the UF Department of Geography.

## Slide 3: Coordinate systems
Why do we need coordinate systems for spatial data?
What is it?

## Slide 4: What is wrong in this map?

## Slide 5: Coordinate, is it simple?
2D flat map
3D sphere

## Slide 6: Two Types of Coordinate System
2D flat, Projected Coordinate System
3D sphere
Geographic Coordinate System

## Slide 7: Coordinate system
Geographic coordinate systems
  A geographic coordinate system (GCS) uses a three-dimensional spherical surface to define locations on the earth.

## Slide 8: Spherical Coordinate System: Graticule
Graticule of meridians and parallels
Longitude and latitude
Units: Degrees (DMS or DD)
Where are the great circles and the small circles?
Notes: Equator: The line of latitude midway between the poles

## Slide 9: Working with Degrees
1°= 60’
1’ = 60”
1° = 60’ x 60” = 3600”
DMS: 51° 29' 16"  DD: 51.4877
29 minutes = 29/60 = 0.4833 degrees 16 seconds = 16/3600 = 0.0044 degrees
51° + 0.4833 ° + 0.0044 ° = 51.4877 °
23.2256 = 23° ? ' ? "
0.2256° * 60 = 13.536'  0.536' * 60 = 32.16”
23.2256° = 22° 13 ' 32.16 "
DMS (degree, minute, second) DD (decimal degree)

## Slide 10: What is WGS_1984?
We need to know the things behind the name

## Slide 11: A few terms
Geoid
Ellipsoid and spheroid
Datum

## Slide 12: The Shape of the Earth

## Slide 13: The Geoid
Another model of the earth’s surface
3-D surface defined by empirical (measured) data that describes the constant gravitational potential, rather than mathematically. (i.e. the surface of the earth's gravity field)
Coincides well with mean sea level for entire planet
Reference surface for vertical position (elevation or height)
Used in conjunction with the ellipsoid to define vertical datum

## Slide 14: Spheroid/Ellipsoid
We think of the
earth as a sphere
It is actually a spheroid, slightly larger in radius at the equator than at the poles
Equatorial circumference = 40,705 km
Polar circumference = 40,008 km
Notes: Ellipse

## Slide 15: Define an Ellipsoid
A mathematical model of the earth must be selected.
P
F2
O
F1
a
b
X
Z


O
X
Y
a
a
b
Rotational axis
For the earth:
Major axis, a = 6378 km
Minor axis, b = 6357 km
Flattening ratio, f = (a-b)/a ~ 1/300
Notes: More correctly, the Earth is an ellipsoid, a special or specific case of spheroid: the oblate spheroid class

## Slide 16: Official Ellipsoids
Many others too!
Why more than one?
Notes: Why more than one?
Notice the Year column
What do you think measurement technology might have been like?
  Think about geographic extent
Many others too…

## Slide 17: Summary
Surface = The Earth’s real surface, all the mountains, depressions, etc.
Geoid = Bumpy surface. Surface of constant gravitational potential (which varies locally) empirically defined by a system of data where gravity is equal for all locations. Measurement equipment: Gravimeter.
Ellipsoid = Ideal, smooth surface, mathematically defined by the semi-major and semi-minor axes.

## Slide 18: Datums
A datum defines the position of the spheroid relative to the center of the earth.

## Slide 19: Global vs. Local Datum
1. Ellipsoid with a spherical coordinate system and an origin

## Slide 20: Global vs. Local Datum
Global datum
  Datum uses the earth's center of mass as the origin
Local datum
  A local datum aligns its spheroid to closely fit the earth's surface in a particular area.
  A point on the surface of the spheroid is matched to a particular position on the surface of the earth. (The origin point of the datum)
  The coordinate system origin of a local datum is not at the center of the earth.

## Slide 21: Common Global vs. Local Datum
Common Local Datum
  North American Datum (NAD)
  Australian Geodetic Datum (AGD)
  European Geodetic Datum (EGD),
  Tokyo Datum (TD)
Common Global Datum
  World Geodetic System (WGS)

## Slide 22: Principal Datums Used in USA
North American Datum of 1927 (NAD27)
North American Datum of 1983 (NAD83)
World Geodetic System of 1984 (WGS84)

## Slide 23: NAD 27 and NAD 83
North American Datum - 1927
North American Datum - 1983
26,000 survey stations
250,000 survey stations
And 2,000,000 distance measurements

## Slide 24: WGS84
The datum on which GPS coordinates are based and probably the most common datum for GIS data sets with global extent. Devolped by DoD.
World Geodetic System - 1984

## Slide 25: Position Shifts and Datums
Incorrect datum  a mismatch of the positions of mapped features.
Errors approaching one kilometer (this is a worst-case scenario, and unlikely).
As long as the two datums in question are known, conversion is possible in GIS.

## Slide 26
East-West Datum Shift with NAD27 and NAD83

## Slide 27: North-South Datum Shift with NAD27 and NAD83

## Slide 28: Horizontal vs Vertical Datums
Horizontal datums are the reference values for a system of location measurements.
Vertical datums are the reference values for a system of elevation measurements.
  The job of a vertical datum is to define where zero elevation is, this is usually done by determining mean sea level, a project that involves measuring tides over a cycle of many years.

## Slide 29: Vertical Datums
A “zero surface” from which all elevations or heights (e.g. of mountain peaks) are measured.
Usually the mean sea level (MSL) is used as the vertical datum globally
Local vertical datums are defined for use in specific geographic areas and rely on locally determined MSL readings, aka. shoreline height
Common vertical datums for the USA are National Geodetic Vertical Datum of 1929 (NGVD29) and North American Vertical Datum of 1988 (NAVD88)

## Slide 30: Projected Coordinate Systems

## Slide 31: Flattening the Earth:
You will often use a Cartesian coordinate system (squared grid)
How do you go from the round Earth to a flattened map and coordinate system?
We need Projected coordinate system

## Slide 32: What are projected coordinate systems?
A projected coordinate system is defined on a flat, two-dimensional surface.
Unlike a geographic coordinate system, a projected coordinate system has constant lengths, angles, and areas across the two dimensions.
A projected coordinate system is always based on a geographic coordinate system

## Slide 33: Map Projection
The systematic rendering of a graticule on a flat map surface
Why? Because globes are difficult to digitize…carry in your pocket…measure the distance from here to JAX, etc.
Easier to read a flat map
Perspective does not influence the view of the information
Real-world features must be projected with minimum distortion from a round earth to a flat map; and given a grid system of coordinates.

## Slide 34: Specifications for Map Projections
Location of light source
  Ellipsoid center  Gnomonic projection
  Antipode  Stereographic projection
  Infinity (off of ellipsoid)  Orthographic projection
Projection Surfaces
  Planar
  Cylindrical
  Conic
Location of the projection surface
  Tangential vs. Intersecting aka Secant
  Orientation of the projection surface relative to the equator and poles

## Slide 35: Projection Light Source
The position affects the resulting map.
  Gnomonic: globe center (light source 1)
  Stereographic: on globe surface, opposite the projection surface (light source 2)
  Orthographic: off globe surface at distance infinity (light source 3)

## Slide 36: Projection Surfaces
The “physical” surface used to construct a map
  Plane – starts flat, stays flat
  Developable surface – starts “rolled”, ends flat

## Slide 37: Three Common Projection Surfaces
(The red indicates contact between the sphere and the projection surface.)
tangent – being in contact at a single point or along a line
Cylinder
(Cylindrical)
tangent
Plane
(Planar or Azimuthal)
tangent
Cone
(Conic)
secant
secant – cutting, intersecting

## Slide 38: Planar and Azimuthal Projections

## Slide 39
Conic Projections
(North up)

## Slide 40
Oblique
Transverse
Cylindrical Projections
Regular

## Slide 41: Cylindrical Projections
Regular
Oblique
Transverse

## Slide 42: Distortion during Map Projection
Bolstad, Fig. 3-16
I = intersection pts (aka
Standard Lines or Parallels)
A,B,D,E = map surface edge
a,b,d,e = scaled map surface

## Slide 43: Map Projection & Distortion
Shape (conformal) - If a map preserves shape, then feature outlines (like county boundaries) look the same on the map as they do on the earth.
Area (equal-area) - If a map preserves area, then the size of a feature on a map is the same relative to its size on the earth.
Distance (equidistant) - An equidistant map is one that preserves true scale for all straight lines passing through a single, specified point. If a line from a to b on a map is the same distance that it is on the earth, then the map line has true scale. No map has true scale everywhere.
Direction/Azimuth (azimuthal) – An azimuthal projection is one that preserves direction for all straight lines passing through a single, specified point.
Converting a sphere to a flat surface results in distortion.

## Slide 44: Common US/Florida Projections
Distortion least between standard parallels
Good for E–W extensive study areas
Conformal: Azim. angles measured locally are correct

## Slide 45: Alerts Equal Area Conic
Areas proportional to those on earth
Distortion least between standard parallels
Good for E/W-extensive study areas
Best for mid-latitudes
Used by Florida Geographic Data Library, many agencies in Florida

## Slide 46: Common US/Florida Projections
Distortion least near central meridian
Good for N/S-extensive study areas
Conformal, so OK for navigation (like normal Mercator)

## Slide 47: Universal Transverse Mercator Coordinate System
World divided into 60 six-degree-wide zones
  Wide zones good for large study areas
  But, coordinates discontinuous across zone boundaries
From 80S to 84N
Zones numbered 1-60 (N&S), W to E, starting at 180W
Excellent discussion in Bolstad (pp. 80-82): read!

## Slide 48: UTM Grid Overlay
1
60
60 Zones, and 20 Latitude Bands
17
G
M
W
X
80º S
84º N
D
C
E
F
H
J
K
L
N
P
Q
R
S
T
U
V
Latitude Bands
17R
R
Zones
Equator
http://www.dmap.co.uk/utmworld.htm
Notes: Universal Transverse Mercator
Note: The grid shown in the example is not drawn to scale.
There are sixty UTM zones, running north-south, cover all of the earth, beginning with zone 1 located at 180º W longitude. Twenty latitude bands, running east-west, cover most of the earth from 80º S latitude to 84º N latitude. The polar regions are covered by the Universal Polar Stereographic coordinate system, which is based on the UTM system. Notice that the letters “I” and “O” are not used to designate a latitude band. This is to prevent confusion with the numbers 1 and 0. The equator separates latitude bands N (north of the equator), and M (south of the equator). If a GPS receiver is showing a position with a latitude band letter of C through M, then it thinks it’s in the southern hemisphere. If the latitude band letter shown on a GPS receiver display is N through X then the receiver thinks it’s position is in the northern hemisphere. Either hemisphere could have exactly the same easting and northing coordinates representing two different locations (one in each hemisphere) within the same zone.
Zones and latitude bands make up 1,200 unique grid rectangles in the UTM grid system. A UTM zone is 6° wide (remember, it’s based on longitude) and extends from 80° south latitude to 84° north latitude. By knowing the correct zone number and latitude band letter, you can narrow your location from the entire surface of the earth down to a rectangle 6° x 8°, as shown in the example above with “21T.” The easting and northing numbers refine the position to a single point somewhere inside that rectangle.
Try this test with your GPS receiver. Set your receiver coordinate system to UTM. Get a UTM position where you live, and save it as a waypoint. Now change the coordinate system in the receiver to latitude and longitude (it doesn't matter which format you select). Then edit the waypoint in lat/long by changing just the longitude to a new value. For example, if the original waypoint longitude shows 115 10' 30", change the degrees from 115° to 90. Save the modified waypoint, and change the lat/long coordinate system back to UTM in the receiver's setup page. Now look at the saved waypoint once again in UTM. Notice how the UTM zone number has changed to match the edited longitude. Try the same test again, only this time leave the coordinates in UTM. Edit the northing coordinate by a large amount and notice how the latitude band changes automatically the moment you save the edited waypoint.

## Slide 49: UTM Zones in the Contiguous U.S.
1260
1200
1140
1080
1020
960
900
840
780
720
660
10
11
12
13
14
15
16
17
18
19
UTM Zones
Longitude
Notes: UTM Zones Covering the Contiguous U.S.
The continental United States lies within ten UTM zones. Zone boundaries are determined by longitude meridians six degrees apart.

## Slide 50: UTM Zones - Side by Side
Equator
840 N
800 S
60
60
60
60
60
60
Notes: UTM Zones - Side by Side
The 60 zones that make up the UTM coordinate system are independent of each other, and have no association with each other. The poles are covered by the Universal Polar Stereographic (UPS) coordinate system. In the northern hemisphere the UTM grid ends at 84º north latitude, and in the southern hemisphere it ends at 80º south latitude. At the equator each UTM zone is less than a million meters wide, so no UTM zone ever exceeds one million meters in width (hence only six digits are required in easting coordinate values). At 84º N latitude, each UTM zone is less than 200,000 meters wide. This is because the longitude lines that form UTM zones converge as they get closer to the poles.

## Slide 51: State Plane Coordinate System
Underlying projections:
  Lambert Conformal Conic for “east-west” areas
  Transverse Mercator for “north-south” areas
  Oblique Mercator for Alaska
Local FIPS (Federal Information Processing Standards) zone (name or number) must be specified in GIS (e.g., any of three in Florida) when projecting into state plane
Specify datum and units, too…
But no “projection parameters”
US only
Notes: Federal Information Processing Standards
FIPS zones on many Web sites, often in GIS Help

## Slide 52: Map of SPC Systems
The solid yellow lines indicate zones

## Slide 53: State Plane Coordinate System
Divides the US into 120 sections, referred to as zones. Each zone is assigned a code number that defines the projection parameters for the region.
Zones that lie north-south (New Jersey) use the Transverse Mercator projection; zones that lie east-west (Tennessee) use the Lambert Conformal Conic.
Developed in the 1930s by the US Coast and Geodetic Survey to provide a common references system for highway engineering, survey marker location, and other high-precision needs.
Goal was to design a conformal (preserve shapes) mapping system for the country with a maximum scale distortion of one part in 10,000, then considered the limit of surveying accuracy.
Four times more accurate than UTM.

## Slide 54: Different Projections

## Slide 55: Differences between Projections

## Slide 56: What is wrong in this map?

## Slide 57: Working with Coordinate System in GIS
Projection in ArcGIS
  Projection define
    Select a predefined projection
    Import from a file which has projection defined
    Define by your own
  Projection transform
On-the-fly Projection